## Slide 1
Improving Deep Learning Performance: Strategies for Enhancing Tensor Cores and Neural Processing Units
PRESENTED BY
X-PURA
PAGE 01
Abdallah Awad, Ali Al-Saed, Osama Hamdan
Instructor: Dr.Aymen Hroub

## Slide 2
X-PURA
PAGE 02
Problem Definition
- NPUs face two main issues:
1. Inefficiency in FP16 multiplication within Tensor Cores.
2. Bottlenecks caused by limited vector lengths in SoftMax
operations during transformer computations.
- These challenges hinder performance scalability and latency reduction in AI workloads.
Optimizing these areas is crucial for handling advanced neural network tasks like transformers.
Introduction to the Problem
Relevance

## Slide 3
X-PURA
PAGE 03
Research Objectives
- Develop an advanced FP16 multiplier using the Karatsuba algorithm to reduce computational complexity.
- Enhance the vector unit architecture by increasing its length to improve parallel processing.
- Optimize NPUs to balance performance with resource and energy efficiency.
Key Goals
Expected Outcomes
-Achieve higher throughput and lower execution times for AI workloads.
- Provide scalable solutions adaptable to future AI models.

## Slide 4
Contributions
X-PURA
PAGE 04
- Development of a novel FP16 multiplier leveraging the Karatsuba algorithm for reduced computational complexity.
- Extension of vector unit length from 512 to 1024 bits for improved parallelism in SoftMax.
- Comprehensive performance evaluations comparing the proposed solutions to classical methods.
CORE CONTRIBUTIONS
- Enables NPUs to efficiently handle transformer models and large-scale neural networks.
- Provides a foundation for energy-efficient, high-performance AI accelerators.
IMPACT

## Slide 5
X-PURA
PAGE 05
Major Related Works
Efficient mixed-precision computation with FP16 multipliers and FP32 accumulators.
NVIDIA TENSOR CORES
Focus on flexibility and programmability, targeting AI-specific operations like SoftMax.
INTEL NPUS
Limited scalability and inefficiencies in vectorization for AI accelerators.
GAPS IDENTIFIED
Existing Innovations

## Slide 6
X-PURA
PAGE 06
Proposed Solution
- A divide-and-conquer method that splits numbers into smaller components for efficient multiplication.
- Reduces computational complexity to Θ(n^1.585), enabling faster FP16 multiplications.
Karatsuba Algorithm
Vector Length Expansion
- Extending vector length from 512 to 1024 bits allows simultaneous processing of more data.
- Mitigates performance bottlenecks in SoftMax operations common in transformer models.

## Slide 7
X-PURA
PAGE 07

## Slide 8
X-PURA
PAGE 08
Methodology
- Modify Tensor Core design to include the Karatsuba multiplier for FP16 operations.
- Expand vector unit length while maintaining compatibility with existing NPU architectures.
IMPLEMENTATION APPROACH
- Compare execution times and throughput of the Karatsuba algorithm versus classical multiplication methods.
- Assess vector unit performance across different lengths (e.g., 512, 1024, 2048 bits).
- Use metrics such as execution time, throughput, and resource utilization to validate improvements.
EVALUATION FRAMEWORK

## Slide 9
X-PURA SIMULATOR

## Slide 10
X-PURA
Snapshot from Results
PAGE 09

## Slide 11
X-PURA
Snapshot from Results
PAGE 09

## Slide 12
X-PURA
PAGE 10
Experimental Results
- Execution time reduced by approximately 2x compared to classical methods.
- Achieved a throughput of 9111.55 tasks/second versus 4231.74 tasks/second for classical multiplication.
Karatsuba Algorithm
- Optimal performance observed with a 2048-vector length, offering the lowest execution time.
- 1024-vector length provides a balance between efficiency and hardware resource requirements.
Vector Length Impact
- Increased vector lengths reduce the number of tasks needed to complete workloads, improving efficiency.
- Karatsuba multiplier shows significant scalability and resource savings.
Key Observations

## Slide 13
X-PURA
PAGE 11
Results and Plots

## Slide 14
X-PURA
PAGE 12
Analysis, Discussions, and Comparisons
- Proposed solutions outperform existing methods in terms of execution time, throughput, and task efficiency.
- Demonstrated scalability for large-scale AI workloads.
PERFORMANCE COMPARISONS
- Increased vector length requires more hardware resources, leading to potential trade-offs in area and power consumption.
- Adapting the Karatsuba algorithm to hardware introduces design complexity.
CHALLENGES IDENTIFIED
- Outperforms NVIDIA Tensor Cores and Intel NPUs in SoftMax and matrix multiplication tasks.
STATE-OF-THE-ART BENCHMARKS

## Slide 15
X-PURA
PAGE 14
Conclusion and Future Work
- Combined use of the Karatsuba algorithm and vector length expansion enhances NPU performance.
- Improved computational efficiency and throughput for AI applications.
SUMMARY OF ACHIEVEMENTS
- Explore energy-efficient designs for mobile and edge devices.
- Investigate scalability for more complex neural networks and larger datasets.
- Incorporate additional algorithms for further optimization.
FUTURE DIRECTIONS

## Slide 16
Thank
You!
X-PURA
PAGE 15